## Slide 1: Convergence in High-rate Structural Health Monitoring and Prognostics for Millisecond Decisions Intern Work Summer 2025
Presenter: Ryan Yount1
and Dr. Adriane Moura & Dr. Alain Beliveau 1 Applied Research Associates Inc.

## Slide 2: Outline of Topics
Introduction
  High-rate Structural Health Monitoring
    High-rate dynamics
    Drop testing
  Kriging
Methodology
  Experimental setup
    Specific drop testing
    Intentional failure mechanisms
  Kriging model
  Optimization loop
Results
Conclusions

## Slide 3: Introduction

## Slide 4: High-Rate Dynamics
A dynamic response with
  High-rate (on the order of < 100 ms)
  High-amplitude (acceleration > 100 gn)
Induces transient states in system, exciting system frequencies
Can lead to unpredictable responses in structural integrity of components
Blast against civil structures
Automotive impact and crashes
High Speed aircraft and airframes
Lightning Strikes on aircraft

## Slide 5: High-Rate Structural Health Monitoring (SHM)
Goal:
Determine condition of a structural system and make system decisions in less than a millisecond, while structure sustains unknown/unmeasured, high-magnitude, and short-duration impacts
Challenges:
  Adequate sensing awareness (time, space, and frequency)
  System knowledge of approximate dynamics
  Uncertainty in loading
  Resources for algorithm implementation
The high-rate structural health monitoring problem has multiple time-scales to address:
Time scales of… | Time Scales | Examples
duration of the event | 30 µs – 100 ms | Structural loading - blast, high-speed impact, automotive crash
sensor response | 3 µs – 10 µs | Accelerometer, strain gage, etc.
different physical behavior regimes | 250 µs – 1 sec | Energy propagation, structural resonance
algorithm execution and decision-making | 100 µs – 1 ms | Damage detection, uncertainty quantification, state awareness, decision making
High-Rate | 1 ms
Very High-Rate | 100 us
Ultra High-Rate | 1 us

## Slide 6: Project Overview
Converge the foundational technologies for the high-rate challenge into a common knowledge product through a common dataset
Use an extended progressive damage dataset of a DoD-relevant electronics package subjected to repeated shock loading to enable interchangeability between efforts focused on different high-rate challenges
Summer Internship Goal:
Generate dataset of higher energy impact failures (low cycle failures) on electronics board of interest

## Slide 7: Drop Testing
Simulates high-speed impacts to assess performance and durability of materials, components, or structures
Drops a guided mass with a test structure onto an anvil
Hard to gather large amounts of datapoints at specific peaks and pulse widths

## Slide 8: Kriging Interpolation
Spatial interpolation technique used to estimate values at unmeasured locations based on known values at nearby locations (commonly used in geostatistics)
Uses spatial autocorrelation and a variogram
  Says points that are closer together are more likely to be similar than points that are farther apart
  Function that models the spatial autocorrelation in the data to determine the weights used in the interpolation
Reduces the number of data points needed to characterize experimental domains
  Especially used in cases where it is difficult to sample datapoints
Project Application:
  Use Kriging Interpolation to decide next point to test to populate common dataset over range of impact conditions (peak and duration)
Next test point
https://geobgu.xyz/r/spatial-interpolation-of-point-data.html
Annual Rainfall Prediction – Ordinary Kriging

## Slide 9: Methodology

## Slide 10: Experimental Setup
Drop tower
  Find references for the peak acceleration (kgn) and pulse width (µs) to test
  Repeat the same peak and pulse width area for an attached test structure until a failure in the resistor occurs
Fixed-fixed printed circuit board
  Accelerometer to monitor board
  Resistor as failure component
Resistor
Side view
Top view
Accelerometer

## Slide 11: Experimental Setup
Resistor attached to board
  Meant to “fail” (detach)
  Solder joints need to be controlled
Track the amount of solder used to attach the part
  Use a stencil
  Tests are more repeatable
Impact each board at specific conditions to build a dataset

## Slide 12: Experimental Setup
No Failure
Failure

## Slide 13: Kriging with Iterative Spatial Prediction of Uncertainty (KRISP-U)
Algorithm uses Leave-One-Out (LOO) cross-validation to estimate the uncertainty of the model spatially
Compares full model, , to a model missing one-point, using Kullback-Leibler divergence
  KL divergence measures how one probability distribution differs from another by quantifying the “distance”
Once that is done for each point, a full variance map is generated and suggested future points are provided
  Max uncertainty
  Uncertainty centroid thresholds of 0.3, 0.5, 0.7

## Slide 14: Results

## Slide 15: Initial Data for Kriging Model
Populate the bounds of the experimental design space
  Goal: 1 hit failures for upper bounds and >5000 gn impacts for lower bound (upper limit of USC dataset)
Populate a few interior data points
Provide this data to the Kriging Model to generate next condition to test at

## Slide 16: Results – Iteration 1
MAE = 0.6907 RMSE = 1.1415 = 348.4093
Next point to test

## Slide 17: Results – Iteration 3
MAE = 0.7147 RMSE = 1.0088 = 178.2139
Next point to test

## Slide 18: Results – Iteration 7
MAE = 1.002 RMSE = 1.4055 = 237.305
Next point to test

## Slide 19: Results – Frequency Analysis
Previous work also investigated the ability to utilize frequency analysis on edge devices for fast responses
A shift in the natural frequency is observed with the failure of the resistor (fell off the board) at impact 6
With resistor
Resistor failure

## Slide 20: Optimization Loop
Utilizing the ability to manipulate the drop tower to hit at different “conditions” and the suggestion for future points from the Kriging model, we can loop around to get more datapoints to build the model up
A sufficient model could be deployed on the edge to quickly estimate impacts to damage after an impact occurs

## Slide 21: Conclusions

## Slide 22: Conclusions
Solder joint quality plays an important role in the ability of the component to handle shock
  Possibly equal or more important than the amount of solder
If a kriging model can be perfected, the finished model could be deployed onto a HR-SHM enabled device
  Faster “impacts-to-failure” calculations also means faster decision-making
Modal frequencies in the board are noticeably different after a resistor detachment

## Slide 23: Future Work
Investigate the effectiveness of different methods of reflow soldering the component for consistency in solder joint quality
Add to the dataset with hit locations from the drop tower at the University of South Carolina
Fusion of high-speed dynamic data with model-based data
Implement computing and decision-making on-the-edge

## Slide 24: Acknowledgements
FY24 AFRL/RW Chief Scientist Innovative Research Fund “Munition Health Monitoring during Maritime Engagements”
FY25 AFOSR LRIR 25RWCOR006 “Convergence in High-rate Structural Health Monitoring and Prognostics for Millisecond Decisions”

## Slide 25: References
[1] R. Yount, T. Roberts, J. Dodson, A. Moura, and A. R. J. Downey, “Experimental Analysis to Enable Low- Latency Structural Health Monitoring for Electronics in High-Rate Dynamic Environments,” in Data Science in Engineering Vol. 11, Cham: Springer Nature Switzerland, 2025.
[2] J. Dodson, A. Downey, and S. Laflamme, “High-rate Structural Health Monitoring: Part-I Introduction & Data,” in IMAC 41, Feb. 2023.
[3] Dodson, J. et al. (2022). High-Rate Structural Health Monitoring and Prognostics: An Overview. In: Madarshahian, R., Hemez, F. (eds) Data Science in Engineering, Volume 9. Conference Proceedings of the Society for Experimental Mechanics Series. Springer, Cham. https://doi.org/10.1007/978-3-030- 76004-5_23

## Slide 26: Data Appendix

## Slide 27: Test Set 1

## Slide 28: Test Set 1 – m014_8KG

## Slide 29: Test Set 1 – m014_p5KG

## Slide 30: Test Set 1 – m014_p10KG

## Slide 31: Test Set 1 – m018_9KG

## Slide 32: Test Set 1 – m018_p10KG

## Slide 33: Test Set 1 – m116_p5KG

## Slide 34: Test Set 1 – m116_p8KG

## Slide 35: Test Set 1 – m116_p12KG

## Slide 36: Test Set 1 – m116_p15KG

## Slide 37: Test Set 1 – m018116_p6KG

## Slide 38: Test Set 2

## Slide 39: Test Set 2 – m018x1_p6KG

## Slide 40: Test Set 2 – m018x1_p8KG

## Slide 41: Test Set 2 – m018x1+T_p6KG

## Slide 42: Test Set 2 – m018x1+T2_p5-5KG

## Slide 43: Test Set 2 – m018x1+T2_p5-5KG2
No board data

## Slide 44: Test Set 2 – m018x1+T3_p5-5KG
No board data

## Slide 45: Test Set 2 – m116x2_p10KG
No board data

## Slide 46: Test Set 2 – m316x1_p6KG
No board data

## Slide 47: Datapoints

## Slide 48: Datapoints
Datapoints 1
X Y Z
175.562 5.38749 65
99 12.211 2
329.89 5.402 19
218.02 10.466 1
132.23 7.692 2
144.5 10.254 4
186.8 9.788 1
251.7 8.162 3
205 9.364 1
Datapoints 2
X Y Z
175.562 5.38749 65
99 12.211 2
329.89 5.402 19
218.02 10.466 1
132.23 7.692 2
144.5 10.254 4
186.8 9.788 1
251.7 8.162 3
205 9.364 1
164 10.26 1
Datapoints 3
X Y Z
175.562 5.38749 65
99 12.211 2
329.89 5.402 19
218.02 10.466 1
132.23 7.692 2
186.8 9.788 1
251.7 8.162 3
205 9.364 1
164 10.26 1
185.3 8.8582 3
Datapoints 4
X Y Z
175.562 5.38749 65
99 12.211 2
329.89 5.402 19
218.02 10.466 1
132.23 7.692 2
324.07 6.235 8
186.8 9.788 1
251.7 8.162 3
205 9.364 1
164 10.26 1
185.3 8.8582 3

## Slide 49: Datapoints
Datapoints 5
X Y Z
175.562 5.38749 65
99 12.211 2
329.89 5.402 19
218.02 10.466 1
132.23 7.692 2
324.07 6.235 8
186.8 9.788 1
251.7 8.162 3
205 9.364 1
164 10.26 1
185.3 8.8582 3
207.67 6.11 13
Datapoints 6
X Y Z
175.562 5.38749 65
99 12.211 2
329.89 5.402 19
218.02 10.466 1
132.23 7.692 2
324.07 6.235 8
318.62 6.47 3
186.8 9.788 1
251.7 8.162 3
205 9.364 1
164 10.26 1
185.3 8.8582 3
207.67 6.11 13
Datapoints 7
X Y Z
175.562 5.38749 65
99 12.211 2
329.89 5.402 19
218.02 10.466 1
132.23 7.692 2
324.07 6.235 8
318.62 6.47 3
186.8 9.788 1
251.7 8.162 3
205 9.364 1
164 10.26 1
185.3 8.8582 3
207.67 6.11 13
211.595 6.045 6
Datapoints 8
X Y Z
175.562 5.38749 65
99 12.211 2
329.89 5.402 19
218.02 10.466 1
132.23 7.692 2
324.07 6.235 8
318.62 6.47 3
186.8 9.788 1
251.7 8.162 3
205 9.364 1
164 10.26 1
185.3 8.8582 3
207.67 6.11 13
211.595 6.045 6
222.92 5.356 6

## Slide 50: Media

## Slide 51: Camera

## Slide 52: Microscope Camera

## Slide 53: High Speed Videos
TS2 – m018x1_p6KG
TS2 – m316x1_p6KG

## Slide 54: MATLAB Scripts

## Slide 55: Script – Set 1 Processing

## Slide 56: Script – Set 2 Processing

## Slide 57: Script – Set 2 Processing